## Slide 1: CCI
Scott Atchley, David Dillow, Galen Shipman
Oak Ridge National Laboratory
Patrick Geoffray
Myricom
Jeffrey Squyres
Cisco Systems, Inc.
George Bosilca
University of Tennessee
Ronald Minnich
Sandia National Laboratories, Livermore
Common
Communication
Interface

## Slide 2: Applications are increasingly data-driven distributed services.
These applications may control only one side of the pipe…
  Common language: IP on the wire, Socket interface on the host.
  Applications: web services, media delivery, trading exchange.
  Not going away, way too much legacy.
Or both sides of the pipe
  No required wire protocol or programing interface.
  Applications: back-ends, database, storage
    Memcached, Big Table, Cassandra.
  Socket interface hinders networking innovation.
  Many vendor-specific interfaces available (dead or alive).
Notes: Service Oriented Architectures Data intensive applications
Inter process communications

## Slide 3: What if you control both sides ?
Application developers either:
  Stick with Sockets.
    See substantially less benefit from current generation network technologies.
  Lock themselves with a vendor-specific interface.
  Support a number of different interfaces.
    Requires deep expertise in multiple low-level network APIs
Network vendors either:
  Port Sockets on their low-level interface.
    Limited performance.
  Push their interface as the solution.
    Everybody loves a good lock-in.
  Support a number of different applications.
    High support costs relative to potential revenue for niche applications.
We propose CCI to satisfy both application developers’ and network vendors’ needs.

## Slide 4: Insulation benefits both
Application Developers
Networking Technology
Vendors

## Slide 5: CCI design goals
Performance
  Utilize OS-bypass, zero-copy, one-sided, asynchronous operations if available.
  Performance portable across host-based implementations and high-end offloaded implementations.
Portability
  Developers have limited resources.
  Provide common abstraction across a wide-variety of networking technologies.
  Avoid vendor lock-in through a vendor neutral API.
Simplicity
  Must not be so complicated that only experts can use it.
  Provide the right balance of functionality without sacrificing simplicity.
  Complexity tends to increase code size and maintenance cost.

## Slide 6: CCI design goals
Scalability
  Dynamic process management: peers come and go – not statically known a priori.
  Approaching 10^6 nodes and 10^9 cores.
  Time (polling) and space (buffer) cannot grow linearly with number of peers.
Robustness
  Failures increase with component count.
  Need to contain faults to a single peer (i.e. fault isolation).

## Slide 7: The landscape
Sockets
MPI
Specialized
Notes: I would stick to one slide for Socket an one for MPI, focusing on semantic differences. I would not present the various specialized ones, just one to show the semantic differences (matching, etc.).

## Slide 8: Sockets
Most widely used
  Simple API
  Robustness (failure tolerant)
  Implicit buffering
  Ubiquitous
Unable to exploit many of the features of current-generation networking technologies
  Cannot support zero-copy
  Does not scale
    In time: linear polling or interrupts.
    In space: per socket resources.
Notes: Epoll (in kernel, requires interrupt)
Could use UDP but no reliability

## Slide 9: MPI
Designed as a bridge between application developers’ and network vendors’ needs in the High Performance Computing market
  Standardization began nearly two decades ago
MPI is the de-facto standard in HPC, Why not elsewhere?
  High level of complexity
    200+ functions in MPI-1, 300+ in MPI-2
  Original standard ignored dynamic environments
    Added later but not widely adopted
  Rigid fault model
    Common fault case is abort execution of entire distributed application
    Robust fault tolerance requires use of MPI dynamic process management (see above)
Notes: Need to bridge was there, the solution was developed but it is narrow in scope (HPC only)
  Later attempts to address dynamic environments have not been widely adopted

## Slide 10: Specialized APIs abound
OFA Verbs
  High level of complexity, vendor lock-in is a concern
Cray/Sandia’s Portals
  Highly specialized interface targeted towards HPC (MPI, SHMEM, UPC)
Qlogics’s PSM
  Highly specialized interface targeted towards MPI
Myricom’s MX
  Highly specialized interface targeted towards MPI
IBM’s LAPI and DCMF
  Limited support outside of IBM network technologies
DAPL
  Limited support outside of iWARP capable devices
LBL’s GASnet
  Designed specifically for the needs of UPC
ARMCI
  Designed specifically for the needs of Global Arrays
LNET
  Designed specifically for the needs of Lustre.
BMI
  Designed specifically for the needs of PVFS

## Slide 11: Summing up the landscape
 | Sockets | MPI | Specialized APIs
Portability | + | + | -
Simplicity | + | - | Varies
Performance | - | + | +
Scalability | - | + | Varies
Robustness | + | - | Varies

## Slide 12: CCI Overview
Endpoints
Connections
Communication
  Active Messages
  Remote Memory Access

## Slide 13: CCI Endpoints
Virtualized instance of a device – src/sink of communication
Complete container of resources – queues and buffers
Process may poll or block for event notification
Events for send, recv, connection establishment, etc.
Events may contain resources such as receive buffers
Resource ownership transfers to the process when the event is retrieved
The process eventually returns the event to CCI
  Expected to be returned in a timely manner
  May be returned out of order
Intel E7

## Slide 14: CCI Connections
Per peer - a single endpoint can handle many connections
Lightweight – no dedicated buffers (~120B/peer)
May have multiple connections to the same peer
Use client/server model similar to Sockets and RDMA-CM
Represents reliability and order attributes
  Reliable with Ordered completion (RO)
  Reliable with Unordered completion (RU)
  Unreliable with Unordered completion (UU)
  Multicast Send (MC_TX)
  Multicast Receive (MC_RX)
Facebook data center

## Slide 15: Active Messages
Berkeley AM
  No posted receives
  Handlers run based on address in header
    No adittional progress until handler completes
  Internally managed buffers
CCI Active Messages
  No posted receives, uses internal buffers
  Events only, no handlers
    Event includes pointer to data, its length, and the connection (peer)
  May be inspected, modified, and/or sent in-place
  May be copied out if needed long term
  Limited in size – ideally MTU sized
  No segmenting/reassembly

## Slide 16: CCI RMA
Active messages are not enough
  But they are enough to allow setup of RMA
Zero-copy when supported
Require memory registration
No intra-message order guarantee
  No last byte written last
Write or Read with an optional Fence

## Slide 17: Status and Evaluation
Three Four proof-of-concept implementations
  Sockets, MX, Portals 3.3, Native SeaStar
Sockets
  Uses UDP with one socket per endpoint
  Implements reliability when required
  Implements AM, RMA Write
MX
  Implements AM only
  CCI requests rendezvous when reliability is requested

## Slide 18: Status and Evaluation
Portals 3.3
  Implements multiple endpoints using match bits
  Portals assumes reliability
    CCI requests acks for reliable connections
  Implements AM, RMA Write, Read, and Fence
Native SeaStar
  Implements AM only
  Working on adding RMA

## Slide 19: CCI/MX Performance

## Slide 20: CCI/Portals Performance

## Slide 21: Native SeaStar Performance
Caveats:
Portals provides matching and thread-safety
Portals running on CNL, not Catamount
CCI/SS may require progress thread

## Slide 22: Conclusion
Distributed apps need
  Performance - low latency, high throughput
  To support transient peers and to isolate peer failures
  To support large numbers of peers with bounded resources
  Portable, simple network interface
CCI aims to satisfy these needs
  Uses endpoints to bound time and space resources
  Uses connections to provide peer fault isolation
  Uses low-overhead active messages for small/control messages
  Uses RMA for bulk movement and zero-copy semantics
  Provides good performance
  Simple API
CCI Next steps
  Finish fleshing out TCP and native Portals implementations
  Work is underway to provide Cray GNI, IBM Blue Gene, and InfiniBand Verbs support

## Slide 23: ATTIC
This is all stuff we likely won’t present

## Slide 24: Outline
What do distributed applications need?
Current APIs
CCI Overview
Status and Evaluation
Conclusion

## Slide 25: Simplicity Example
BTL | Lines of Code
Elan | 1,656
MX | 2,333
Portals | 2,469
GM | 2,779
Sockets (TCP) | 4,192
UDAPL | 6,208
OpenIB (Verbs) | 21,574

## Slide 26: OFA Verbs
Based on earlier VIA spec
Does not specify API, just Verbs
Multiple vendor APIs initially
Coalesced into Open-Fabrics Association (OFA)
Two-sided and one-sided
Always asynchronous
Reliable and unreliable
Connection and connectionless modes
Communication requires registered memory
Queue-Pair represents logical connection

## Slide 27: Portals
One-sided (Put/Get)
Uses tags to steer messages to buffers
Connectionless
  Underlying NALs maintain necessary connection state
Most commonly used on large HPC systems
Lustre distributed file system NAL, LNET, was originally based on Portals

## Slide 28: Myricom MX and Qlogic PSM
Similar two-sided, matching API
  Designed to support MPI
Eager for small messages
Zero-copy, rendezvous for large messages
Semi-connectionless
  Target does accept connection requests
  Sender connects before sending
Reliable, in-order matching with out-of-order completion (like MPI)

## Slide 29: IBM LAPI and DCMF
Designed for RS-series and BlueGene P/Q
Some support outside of IBM exists
One-sided and two-sided
Contiguous and non-contiguous memory layout
Transparent link aggregation
DCMF supports ARMCI, GA, MPI, collectives