## Slide 1: CCI
Galen Shipman
Technology Integration
Common
Communication
Interface

## Slide 2: Outline
What do distributed applications need?
Current APIs
CCI Overview
Status and Evaluation
Conclusion

## Slide 3: The context
Application control one side of the pipe:
  Common language: IP on the wire, Socket interface on the host.
  Applications: web service, media delivery, trading exchange.
  Not going away, way too much legacy.
Application controls both sides:
  No required wire protocol or host programing interface.
  Applications: back-ends, database, storage
    Memcached, Big Table, Cassandra.
  Socket interface hinder networking innovation.
  Gazillions of vendor-specific interfaces available (dead or alive).

## Slide 4: The problem
Application developpers:
  Stick with Sockets.
  Lock themselves with a vendor-specific interface.
  Support a number of different interfaces.
Network vendors:
  Cut corners to improve Sockets.
  Push their interface as the Only True One.
  Support a number of different applications.

## Slide 5: Distributed application needs
Dynamic process management
  Peers come and go – not statically known a priori
Scalability
  Approaching 10^6 nodes and 10^9 cores
  Time and space cannot grow linearly with number of peers
Fault tolerance
  Failures increase with component count
  Need to contain faults to a single peer (i.e. fault isolation)

## Slide 6: Distributed application needs
Performance
  Utilize OS-bypass, zero-copy, one-sided, asynchronous operations
Portability
  Developers have limited resources
  Provide common abstraction
  Avoid vendor lock-in
Simplicity
  Must not be so complicated that only experts can use it
  Finding the right balance of functions
  Complexity tends to increase code size and maintenance cost

## Slide 7: Simplicity Example
BTL | Lines of Code
Elan | 1,656
MX | 2,333
Portals | 2,469
GM | 2,779
Sockets (TCP) | 4,192
UDAPL | 6,208
OpenIB (Verbs) | 21,574

## Slide 8: The landscape
Sockets
MPI
Specialized
Notes: I would stick to one slide for Socket an one for MPI, focusing on semantic differences. I would not present the various specialized ones, just one to show the semantic differences (matching, etc).

## Slide 9: Sockets
Most widely used
  Simple API
  Robustness (failure tolerant)
  Implicit buffering
Stream and datagram modes
Connected and connectionless modes
Client/server semantics for connected mode
Asynchrony via buffered sends and receives
  Requires more CPU work which lowers throughput
SOCK_STREAM inherits TCP performance constraints

## Slide 10: MPI
Dominant interface in HPC
Provides scalability
Rich API (i.e. complicated)
Point-to-point, collective, and one-sided
Blocking and non-blocking
Synchronous, asynchronous, and ready modes
Uses communication groups (communicators)
  May include all process or a subset of processes
Does provide a notion of dynamic process management
  Accept(), Connect() immature, infrequently provided, and much less used
  Imposes high overhead, not performant

## Slide 11: MPI
Point-to-point communication use two modes
  Eager and Rendezvous
Each MPI switches modes at different sizes depending on the network being used
  May be tunable, but users don’t want to tune
  May lead to buffer overruns or OOM on the receiver
Does not specify underlying network protocol
Each MPI implements a NAL
Less mature than Sockets
Well-defined standard (but implementations vary)

## Slide 12: MPI
Rigid fault model
  Default mode is all errors trigger abort
  Optionally may have errors return
    Not clear how to handle missing peers
Assumes reliable delivery
Requires ordered matching, but not ordered completion

## Slide 13: Specialized APIs
OFA Verbs
Cray/Sandia’s Portals
Qlogics’s PSM
Myricom’s MX
LBL’s GASnet
DAPL
IBM’s LAPI and DCMF
Others

## Slide 14: OFA Verbs
Based on earlier VIA spec
Does not specify API, just Verbs
Multiple vendor APIs initially
Coalesced into Open-Fabrics Association (OFA)
Two-sided and one-sided
Always asynchronous
Reliable and unreliable
Connection and connectionless modes
Communication requires registered memory
Queue-Pair represents logical connection

## Slide 15: Portals
One-sided (Put/Get)
Uses tags to steer messages to buffers
Connectionless
  Underlying NALs maintain necessary connection state
Most commonly used on large HPC systems
Lustre distributed file system NAL, LNET, was originally based on Portals

## Slide 16: Myricom MX and Qlogic PSM
Similar two-sided, matching API
  Designed to support MPI
Eager for small messages
Zero-copy, rendezvous for large messages
Semi-connectionless
  Target does accept connection requests
  Sender connects before sending
Reliable, in-order matching with out-of-order completion (like MPI)

## Slide 17: IBM LAPI and DCMF
Designed for RS-series and BlueGene P/Q
Some support outside of IBM exists
One-sided and two-sided
Contiguous and non-contiguous memory layout
Transparent link aggregation
DCMF supports ARMCI, GA, MPI, collectives

## Slide 18: CCI Overview
Endpoints
Connections
Communication
  Active Messages
  Remote Memory Access

## Slide 19: CCI Endpoints
Virtualized instance of a device – src/sink of communication
Complete container of resources – queues and buffers
Process may poll or block for event notification
Events for send, recv, connection establishment, etc.
Events may contain resources such as receive buffers
Resource ownership transfers to the process when the event is retrieved
The process eventaully returns the event to CCI
  Expected to be returned in a timely manner
  May be returned out of order

## Slide 20: CCI Connections
Per peer - a single endpoint can handle many connections
Lightweight – no dedicated buffers (~120B/peer)
May have multiple connections to the same peer
Use client/server model similar to Sockets and RDMA-CM
Represents reliability and order attributes
  Reliable with Ordered completion (RO)
  Reliable with Unordered completion (RU)
  Unreliable with Unordered completion (UU)
  Multicast Send (MC_TX)
  Multicast Receive (MC_RX)

## Slide 21: Active Messages
Berkeley AM
  No posted receives
  Handlers run based on address in header
    No adittional progress until handler completes
  Internally managed buffers
CCI Active Messages
  No posted receives, uses internal buffers
  Events only, no handlers
    Event includes pointer to data, its length, and the connection (peer)
  May be inspected, modified, and/or sent in-place
  May be copied out if needed long term
  Limited in size – ideally MTU sized
  No segmenting/reassembly

## Slide 22: CCI RMA
Active messages are not enough
  But they are enough to allow setup of RMA
Zero-copy when supported
Require memory registration
No intra-message order guarantee
  No last byte written last
Write or Read with an optional Fence

## Slide 23: Status and Evaluation
Three Four proof-of-concept implementations
  Sockets, MX, Portals 3.3, Native SeaStar
Sockets
  Uses UDP with one socket per endpoint
  Implements reliability when required
  Implements AM, RMA Write
MX
  Implements AM only
  CCI requests rendezvous when reliability is requested

## Slide 24: Status and Evaluation
Portals 3.3
  Implements multiple endpoints using match bits
  Portals assumes reliability
    CCI requests acks for reliable connections
  Implements AM, RMA Write, Read, and Fence
Native SeaStar
  Implements AM only
  Unreliable only (working on reliability layer)
  Working on adding RMA

## Slide 25: CCI/MX Performance

## Slide 26: CCI/Portals Performance

## Slide 27: Native SeaStar Performance
Caveats:
Portals provides matching and thread-safety
Portals running on CNL, not Catamount
CCI/SS may require progress thread

## Slide 28: Conclusion
Distributed apps need
  Performance - low latency, high throughput
  To support transient peers and to isolate peer failures
  To support large numbers of peers with bounded resources
  Portable, simple network interface
CCI aims to satisfy these needs
  Uses endpoints to bound time and space resources
  Uses connections to provide peer fault isolation
  Uses low-overhead active messages for small/control messages
  Uses RMA for bulk movement and zero-copy semantics
  Can provide good performance
  Simple API