## Slide 1: CCI
Scott Atchley, David Dillow, Galen Shipman
Oak Ridge National Laboratory
Patrick Geoffray
Myricom
Jeffrey Squyres
Cisco Systems, Inc.
George Bosilca
University of Tennessee
Ronald Minnich
Sandia National Laboratories, Livermore
Common
Communication
Interface

## Slide 2: Applications are increasingly data-driven distributed services.
These applications may control only one side of the pipe…
  Common language: IP on the wire, Socket interface on the host.
  Applications: web services, media delivery, trading exchange.
  Not going away, way too much legacy.
Or both sides of the pipe
  No required wire protocol or programing interface.
  Applications: back-ends, database, storage
    Memcached, Big Table, Cassandra.
  Socket interface hinders networking innovation.
  Many vendor-specific interfaces available (dead or alive).
Notes: Service Oriented Architectures Data intensive applications
Inter process communications

## Slide 3: What if you control both sides ?
Application developers either:
  Stick with Sockets.
    See substantially less benefit from current generation network technologies.
  Lock themselves with a vendor-specific interface.
  Support a number of different interfaces.
    Requires deep expertise in multiple low-level network APIs
Network vendors either:
  Port Sockets on their low-level interface.
    Limited performance.
  Push their interface as the solution.
    Everybody loves a good lock-in.
  Support a number of different applications.
    High support costs relative to potential revenue for niche applications.

## Slide 4: Sockets
Most widely used
  Simple API
  Robustness (failure tolerant)
  Implicit buffering
  Ubiquitous
Unable to exploit many of the features of current-generation networking technologies
  Cannot support zero-copy
  Does not scale
    In time: linear polling or interrupts.
    In space: per socket resources.
Notes: Epoll (in kernel, requires interrupt)
Could use UDP but no reliability

## Slide 5: MPI
Designed as a bridge between application developers’ and network vendors’ needs in the High Performance Computing market
  Standardization began nearly two decades ago
MPI is the de-facto standard in HPC, Why not elsewhere?
  High level of complexity
    200+ functions in MPI-1, 300+ in MPI-2
  Original standard ignored dynamic environments
    Added later but not widely adopted
  Rigid fault model
    Common fault case is abort execution of entire distributed application
    Robust fault tolerance requires use of MPI dynamic process management (see above)
Notes: Need to bridge was there, the solution was developed but it is narrow in scope (HPC only)
  Later attempts to address dynamic environments have not been widely adopted

## Slide 6: Specialized APIs abound
OFA Verbs
  High level of complexity, vendor lock-in is a concern
Cray/Sandia’s Portals
  Highly specialized interface targeted towards HPC (MPI, SHMEM, UPC)
Qlogics’s PSM
  Highly specialized interface targeted towards MPI
Myricom’s MX
  Highly specialized interface targeted towards MPI
IBM’s LAPI and DCMF
  Limited support outside of IBM network technologies
DAPL
  Limited support outside of iWARP capable devices
LBL’s GASnet
  Designed specifically for the needs of UPC
ARMCI
  Designed specifically for the needs of Global Arrays
LNET
  Designed specifically for the needs of Lustre.
BMI
  Designed specifically for the needs of PVFS

## Slide 7: Summing up the landscape
 | Sockets | MPI | Specialized APIs
Portability | ✔ | ✔ | ✗
Simplicity | ✔ | ✗ | Varies
Performance | ✗ | ✔ | ✔
Scalability | ✗ | ✔ | Varies
Robustness | ✔ | ✗ | Varies

## Slide 8: Bridging two communities
Application Developers
Networking Technology
Vendors
Notes: We propose CCI to satisfy both application developers’ and network vendors’ needs.

## Slide 9: CCI design goals
Performance
  Can leverage OS-bypass, zero-copy, one-sided, async ops.
Portability
  Developers have limited resources.
  Avoid vendor lock-in through a vendor neutral API.
Simplicity
  Must not be so complicated that only experts can use it.
  Complexity tends to increase code size and maintenance cost.
Scalability
  Dynamic process management: peers come and go – not statically known a priori.
  Time (polling) and space (buffer) cannot grow linearly with number of peers.
Robustness
  Need to contain faults to a single peer (i.e. fault isolation).
Notes:   Performance:
  performance portable across host-based implementations and high-end offloaded implementations.
  Portability:
  Provide common abstraction across a wide-variety of networking technologies.
  Simplicity:
  Provide the right balance of functionality without sacrificing simplicity.
  Scalability:
  Approaching 10^6 nodes, 10^9 cores
  Robustness:
  Failures increase with component count.

## Slide 10: CCI Overview
Endpoints
Connections
Communication
  Active Messages
  Remote Memory Access
Notes: All resources are in the endpoint (shared)

## Slide 11: CCI Endpoints
Virtualized instance of a device – src/sink of communication
Complete container of resources – queues and buffers
An event driven model
  Application may poll or block
  Events include send, recv, connection establishment, etc.
  Events may contain resources such as buffers
    Resource ownership transfers to the application when the event is retrieved
  May be returned out of order
Intel E7

## Slide 12: CCI Connections
Per peer - a single endpoint can handle many connections
Scalable
  no per-peer send/recv buffers
  no per-peer event queues
May have multiple connections to the same peer
Use client/server connection model similar to Sockets
Represents reliability and order attributes
  Reliable with Ordered completion (RO)
  Reliable with Unordered completion (RU)
  Unreliable with Unordered completion (UU)
    Multicast Send (MC_TX)
    Multicast Receive (MC_RX)
Facebook data center
Notes: Not requiring order enables efficient mutli-rail, high-radix network toplogies, and dynamic routing without specialized hardware
Unreliable unordered – enables applications with strict timing constraints that are incompatible with reliable implementations (if my pricing update from the exchange is retransmitted it might as well be dropped)

## Slide 13: Active Messages
Always buffered on both send and receive side
Library manages buffers, not the application
Events only, no handlers on receives
  True handlers are the devil incarnate
  Event includes pointer to data and the connection (peer)
Message may be processed in-place
  Even forwarded in-place
May be copied out if needed long term
Limited in size
  Ideally MTU size to avoid segmenting/reassembly
Notes:   Message may be Forwarded, Modified, Sent in place

## Slide 14: Remote Memory Access (RMA)
RMA communication for bulk-data transfer
  Zero-copy when available
  One-sided operation
  Active message model used for RMA synchronization
Requires explicit memory registration
  Provides broad portability
  Simplified security model
No intra-message or inter-message order guarantee
  No last byte written last
Optional inter-message ordering fence
May be combined with immediate delivery of AM

## Slide 15: Status and Evaluation
Three Four proof-of-concept implementations
  Sockets, MX, Portals 3.3, Native SeaStar
Sockets
  Uses UDP with one socket per endpoint, Implements reliability when required
  Implements AM, RMA Write
MX
  Implements AM only
Portals 3.3
  Implements multiple endpoints using match bits
  Implements AM, RMA Write, Read, and Fence
Native SeaStar
  Implements AM only
  Working on adding RMA

## Slide 16: CCI/MX Performance

## Slide 17: CCI/Portals Performance

## Slide 18: Native SeaStar Performance
Caveats:
Portals provides matching and thread-safety
Portals running on CNL, not Catamount
CCI/SS may require progress thread

## Slide 19: Benefits of a common bridge
Application Developers
Decrease complexity
Port once, run everywhere
Encourage competition among vendors
  Fosters innovation
  Improves cost effectiveness
Mitigates technical and business risk of single vendor solution
Network Technology Vendors
Increases total addressable market
  Deliver performance to the masses
Ability to expose innovation through a modern API
Reduces costs
  Eliminate per application support
  Leverage community development of core API
  Enables an ecosystem
Notes: Like MPI did for HPC

## Slide 20: Conclusion
Distributed apps need
  Performance - low latency, high throughput
  To support transient peers and to isolate peer failures
  To support large numbers of peers with bounded resources
  Portable, simple programing interface
CCI aims to satisfy these needs
  Uses endpoints to bound time and space resources
  Uses connections to provide peer fault isolation
  Uses low-overhead active messages for small/control messages
  Uses RMA for bulk movement and one-sided semantics
  Provides good performance
  Simple API
CCI Next steps
  Finish fleshing out TCP and native Portals implementations
  Work is underway to provide Cray GNI, IBM Blue Gene, and InfiniBand Verbs support

## Slide 21: Call for participation!
We are a bunch of engineers
  We don’t have a website
  We don’t have a logo
  We don’t have a glossy white-paper
  But… We do have deep expertise in communication libraries
We also have a community development model
  Code is currently hosted on a private git-hub
  License model is BSD/Apache style license
  Contributor agreement is Apache style
If you want to help contribute please contact us
Notes: We have over 100 years in combined experience, but we aren’t yet old enough to realize the magnitude of this task, and we know what source-routing is.

## Slide 22: ATTIC
This is all stuff we likely won’t present

## Slide 23: Outline
What do distributed applications need?
Current APIs
CCI Overview
Status and Evaluation
Conclusion

## Slide 24: Simplicity Example
BTL | Lines of Code
Elan | 1,656
MX | 2,333
Portals | 2,469
GM | 2,779
Sockets (TCP) | 4,192
UDAPL | 6,208
OpenIB (Verbs) | 21,574

## Slide 25: OFA Verbs
Based on earlier VIA spec
Does not specify API, just Verbs
Multiple vendor APIs initially
Coalesced into Open-Fabrics Association (OFA)
Two-sided and one-sided
Always asynchronous
Reliable and unreliable
Connection and connectionless modes
Communication requires registered memory
Queue-Pair represents logical connection

## Slide 26: Portals
One-sided (Put/Get)
Uses tags to steer messages to buffers
Connectionless
  Underlying NALs maintain necessary connection state
Most commonly used on large HPC systems
Lustre distributed file system NAL, LNET, was originally based on Portals

## Slide 27: Myricom MX and Qlogic PSM
Similar two-sided, matching API
  Designed to support MPI
Eager for small messages
Zero-copy, rendezvous for large messages
Semi-connectionless
  Target does accept connection requests
  Sender connects before sending
Reliable, in-order matching with out-of-order completion (like MPI)

## Slide 28: IBM LAPI and DCMF
Designed for RS-series and BlueGene P/Q
Some support outside of IBM exists
One-sided and two-sided
Contiguous and non-contiguous memory layout
Transparent link aggregation
DCMF supports ARMCI, GA, MPI, collectives